## Slide 1: TEAM SUPERAWESOMECOOLKIDS
Starring:
Shawn
Joel
Tom

## Slide 2: The Code
There are several important parts of the code that deal with localization and movement
  Linear transformation for North Star
  Wheel encoder positioning
  Fir filtering
  Kalman filtering
  Movement
  PID controller

## Slide 3: Global Coordinate System
The global coordinate begins on base 0 in the middle of the base
The X direction goes positive along the far wall
The Y direction goes positive along the wall on the right side (facing towards the far wall)
Theta is 0 in the X direction and turns positive when turning counterclockwise. From 0 to 2*pi

## Slide 4: Linear Transformations
Each room has different shift and rotate values
Using advanced measuring techniques, we determined the rotations, scaling, and shifting amounts

## Slide 5: transformation code pseudocode
Get the NS x and y values
Build the transformation matrix using the values obtained during measurement
Matrix multiplication with the [x,y] values with the transformation matrix
Scale the value to our global coordinates

## Slide 6: Some REAL code

## Slide 7: Wheel encoder
Delta values are considered as opposed to entirely new positions like North Star
Deltas for left, right, and rear wheels are taken and broken up into x, y, and theta deltas in terms of robot axis using sin and cos
The x and y deltas are then transformed in terms of the global coordinate system
These deltas are added to the previous global pose to get a new one

## Slide 8: Wheel Encoder Code

## Slide 9: Filtering Process
A separate FIR filter exists for the following sensor values:
  NS x
  NS y
  NS theta
  WE wheels
After research, 7-tap filters were chosen for all sensors except NS theta
  Decided that theta was better off unfiltered, so a 1-tap filter with a coefficient of 1 was applied to make this explicit

## Slide 10: FIR Filter Implementation
Code provided on class website was used for filter method of FIRFilter class
Rather than hard-code number of taps, a file format was devised for filters
  List the coefficients one per line
  The number of lines is the number of taps
This allowed for quicker changes

## Slide 11: FIR Filter Code

## Slide 12: Kalman Filter Implementation
Code provided from website was wrapped by a Kalman class
When initialized, a global Pose object is passed in by reference to be stored internally
A filter method was created accepting two Pose objects
  Pose class has method to return its values as a 3-element array
The global Pose is updated according to track output of wrapped kalman filter function

## Slide 13: Kalman Filter Code

## Slide 14: Movement
Movement was handled through two separate functions, moveTo() and turnTo()
An array of poses were defined as ‘goals’, corresponding to the bases around the room
  Bases were determined by room measurement
  Slightly tuned to actual robot movement

## Slide 15: moveTo()
Given destination in global coordinate system, move forward, tracking theta value of goal versus current location
When theta becomes too great, break into turnTo() function
Move with speed according to PID controller
  Gain applied to keep speed at near maximum until goal is near

## Slide 16: moveTo code

## Slide 17: turnTo()
Get turn speed from PID based on error
  Limited turn speeds such that each turn will occur fast enough to avoid accumulation of WE error
Issue turn command until error is below threshold, then break
If over-turning, robot will reverse turn direction

## Slide 18: turnTo code

## Slide 19: PID control
There were 2 different PID controllers used for the project. One was for the driving forward and one was for turning
For the integral error, our window was the last 10 numbers
The derivative uses only the current value and the most recent previous value
The PID loop is fairly arbitrary, so that it can be used by other sensors and applications. This is done by scaling the value into the range [0,1]

## Slide 20: PID tuning
For each PID, we tuned it by using an educated guess, and then testing the robot
For the integral term, we created an adjustable maximum value that depended on the control
After much testing, we decided that both controls should have their values most affected by the Proportional term, and much less by the integral and derivative terms

## Slide 21: PID code